BLG 322E – Computer Architecture
Assigment 2

There are 2 important conditions for setting the timing of processes:
- While reading data from the register, it is enough to run the DR step of the instruction that will read data from the record and the WB step of the instruction that will write data to the registry at the same time. Because the CPU writes data to registers in the first half of the cycle and reads data from registers in the second half of the cycle.
- In branching operation, IF step of the process to be followed must come after the EX step of the branch instruction. Because the branch target address is calculated in the EX stage, and the result is sent directly to the IF stage.

In the chart below, light steps are a prerequisite for dark steps.

First of all, we put NOOP instruction between instructions to set the timing. And let's exclude instructions that could not enter the pipeline from the scheme.
Total amount of penalty is 10 clock cycles.
To minimize the amount of penalty, let's move the locations of instructions as a software-based solution.

Total amount of penalty is 5 clock cycles.